## Slide 1: Accelerating DICe on an FPGA
Atiyeh Panahi, Keaten Stokke
Advisor: David Andrews

## Slide 2: Thank You for Supporting this Project !
Atiyeh Panahi, Keaten Stokke
Advisor: David Andrews

## Slide 3: Accomplishments to Date
HDL Implementation
Beta version nearly finished
  Need guidance on data output format to complete last IP
  FPGA inputs & outputs need to be established
Current system processing is about 1/100th to scale
  Parameter/BRAM/etc scale up required to handle full image size and increased frame count
  Core functionality complete. Not all DICe’s functionality accounted for yet
Not fully functional yet!

## Slide 4: What We’ve Accomplished
Design
DICe software split into multiple IP’s
  Each IP handles a specific function
  Design Modularized to support future development
State machine structured IP’s
  FSM’s enable more control over operations
  Promotes better scalability and performance
Floating-point function improvements
  Removed the “function” keyword; caused timing errors and constraints
  Building functions as FSM’s yielded major clock speedup
  Previous clock speed: <30 MHz; Current clock speed: 150 MHz

## Slide 5: What We’ve Accomplished
MicroBlaze
The Xilinx soft processor is the powerhouse within the system
  Global system controller
  Allows introduction of operating system, middleware, device drivers
  Helps to debug the system
AXI4 Lite Standard Bus
  MicroBlaze controls the system-wide AXI4-Lite bus
  Allows for processor control over each individual IP
  Speeds up testing by bypassing other IP’s
Ethernet Driver
  MicroBlaze will control the Ethernet that streams the FPGA’s inputs

## Slide 6: Vivado Block Design

## Slide 7: Vivado Block Design

## Slide 8: Vivado Block Design

## Slide 9: Vivado Block Design

## Slide 10: Vivado Block Design

## Slide 11: Current Status
Design is working
Successful simulation and synthesis
  Design meets timing constraints
  Identical outputs are produced
Testing Data
Design compares just 2 frames
  Used to verify IP functionality, buffers, end to end flow
  Image size used (x1)
    64*48 = 3,072 pixels, 98,304 bits at 32 bits per pixel (IEEE format)
  Actual image size needed (x100)
    640*480 = 307,200 pixels, 9,830,400 bits at 32 bits per pixel (IEEE format)
  Scaling now only requires parameter changes, not to FSMs, system architecture

## Slide 12: Results
Reference image VS. Deformed image
HDL VS. GUI - Execution time comparison
Linear growth expected!
Testbench | Frequency | HDL Exe Time | DICe Exe Time
64*48 – BRAM | 100 MHz | 3.5 ms | 13 ms/ 58 ms
64*48 – BRAM | 150 MHz | 2.5 ms | 13 ms/ 58 ms

## Slide 13: Results
Resource Utilization
Reports from 150 MHz design

## Slide 14: Results
Simulation Waveforms

## Slide 15: Results
Synthesis Waveforms

## Slide 16: Demo
Let’s show you some of our work in Vivado!

## Slide 17: Next Steps
Full-scale DICe HDL
Scale up BRAM sizing (x100)
  Expecting images of 640*480 = 307,200 pixels
  Handle a much larger frame count
Extend Functionality
  Ability to have multiple subsets (currently just 1)
  Handle various subset shapes (based on required needs)
Network I/O
  Python program to intermediate (start, video conversion, FPGA communication)
  Ethernet IP/Drivers to stream images
  Desired output type? Text file?

## Slide 18: Next Steps
Optimization & Performance
Memory and resources
  Reduce memory and resource usage to account for design scale-up
Increased clock speed
  Current design operates at 150 MHz
  Potential to increase clock speed to 200 MHz
System-wide speed-up
  Leverage ability to parallelize multiple IP’s
  Implement various pipelining techniques
  Compare HDL and HLS results for efficiency
Clean up
  Improve readability of Verilog code
  Will enable ease of future development

## Slide 19: Questions From Us…
Are square subsets okay, or are unique subset shapes required?
Can we assume we will be sticking with black & white video?
Do you want us to set up a GitHub repository of our work and share the link to monitor progress?
Would it be possible to get a screen-recorded video of how your teams use the DICe software on some sample video, along with the total execution time?
I/O specifics for the FPGA

## Slide 20: Questions For Us?